## Slide 1: Nimble Page Management for Tiered Memory Systems
Zi Yan*
Daniel Lustig*, David Nellans*
Abhishek Bhattacharjee✥
*NVIDIA Research, ✥Yale University

## Slide 2: Heterogeneous Memory system
CPU
TLB
GPU
TLB
Accelerator
TLB
Accelerator
TLB
MCDRAM
HBM
Interconnect Network
DRAM
Non-Volatile Memory

## Slide 3: Heterogeneous memory Management
OS page management
Placing pages in memory initially
Relocating pages to other memory
Two key components
Policy: where to place/move pages
e.g., Thermostat1, HeteroOS2
Mechanism: Page migration process
Execute policy decisions
CPU
TLB
GPU
TLB
Acc
TLB
Acc
TLB
MCDRAM
HBM
Interconnect Network
DRAM
Non-Volatile Memory
Page
Page
Page
Mechanism is as important as policy
N. Agarwal et al. Thermostat: Application-transparent Page Management for Two-tiered Main Memory. ASPLOS 2017
S. Kannan et al. HeteroOS: OS Design for Heterogeneous Memory Management in Datacenter. ISCA 2017

## Slide 4: Faster Page Migration = Better PERF
Performance boost over stock Linux
Fast memory
16GB
Slow memory
40GB
CPU
TLB
Disaggregated memory system
Standard Linux page replacement policy
Optimizing page migration mechanism in OS
32GB workloads
Chart: Runtime Speedup
| Geomean
Stock Linux | 1
Optimized Page Migration | 1.3512
40% Runtime Improvement

## Slide 5: Page Migration Throughput Is LOW
Page migration profiling
  Three common manners
  Between two mem nodes
  19.2 GB/s hardware BW
Observations
  Low throughput (4%)
  High kernel overhead
4KB
2MB
2MB

## Slide 6: Page Migration Problems
High kernel overhead
  Locks on shared data structures, e.g. page lists
  Virtual memory maintenance, e.g. page table modification
  Split huge pages before migration
Kernel operation serialization
Migration process serialization
Low throughput
19.2GB/s available hardware bandwidth
 | Base Page (4KB) | 512 Base Pages (2MB) | Split THP (2MB) | Max Copy Throughput
X86_64 | 0.04 GB/s (0.3%) | 0.75 GB/s (5.0%) | 0.75 GB/s (5.0%) | 15.05 GB/s

## Slide 7: The Goals of Improving Page Migration
High performance
Achieve throughput as high as possible
Significantly reduce page migration overheads
Ease of implementation
Implemented in Linux
Reuse most of existing code
Generality
Not rely on special hardware
Applicable to other uses, memory offlining, hot add/remove

## Slide 8: Improve Page Migration System
Policies decide which pages to move
In Linux, move_pages() system call connects policies with the mechanism
The mechanism helps move pages
My work improves the mechanism
Policies
Auto NUMA
Program Controlled
Device Drivers
Mechanism
Allocate new pages
Unmap old pages & TLB invalidation
Copy data from old pages to new pages
Map new pages
Free old pages
System Call move_pages()

## Slide 9: Page Migration Optimizations
Transparent huge page (THP) migration
  Reduce kernel overhead
4KB Data Copy
…
2MB
Data Copy
4KB Data Copy
4KB Data Copy
4KB Data Copy
Time
512 migrations
1 migration

## Slide 10: Page Migration Optimizations
Transparent huge page (THP) migration
  Reduce kernel overhead
Parallel page migration
  Improve data copy throughput
Time
Single-threaded
Data Copy
Multi-threaded
Data Copy

## Slide 11: Page Migration Optimizations
Transparent huge page (THP) migration
  Reduce kernel overhead
Parallel page migration
  Improve data copy throughput
Concurrent page migration
  Parallelize kernel operations
Data Copy
Data Copy
Data Copy
Data Copy
N Concurrent
Data Copies
…
Time
Serialized
Concurrent

## Slide 12: Page Migration Optimizations
Transparent huge page (THP) migration
  Reduce kernel overhead
Parallel page migration
  Improve data copy throughput
Concurrent page migration
  Parallelize kernel operations
Exchange pages
  Reduce migration process overhead
All optimizations can be combined
Time
Node 0
(Full)
Node 1 (Not Full)
Data Exchange
Data Copy 1
Step 1
Data Copy 2
Step 2
Node 0
(Full)
Node 1 (Not Full)
Step 1 & 2

## Slide 13: Page Migration Improvement
Chart: 
| Linux Page Migration | THP Migration | Parallel THP Migration (4 threads) | Parallel Concurrent THP Migration (4 threads) | Parallel Concurrent Exchange THP (4 threads)
 | 0.05 | 0.14 | 0.4 | 0.67 | 0.73
Max achievable data copy throughput: 15GB/s
14.6x improvement

## Slide 14: Methodology
Disaggregated memory in real hardware
  A two-socket NUMA machine
  Fast memory has 2x bandwidth and 1/2 access latency over Slow memory
Experiments run on modified Linux
  Integrate all page migration mechanism optimizations
  Adapt Linux page replacement algorithm as the page migration policy
Benchmarks
  SpecACCEL and graph500
  32GB footprint for each benchmark

## Slide 15: Results
Chart: Speedup over All Slow
| 503.postencil | 551.ppalm | 553.pclvrleaf | 555.pseismic | 556.psp | 559.pmniGhost | 560.pilbdc | 563.pswim | 570.pbt | graph500-omp | geomean
All Slow | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Stock Linux | 1.0057 | 0.94062 | 1.2743 | 1.09 | 0.98922 | 1.0887 | 1.2536 | 1.5281 | 1.0231 | 0.86915 | 1.092
Optimized Page Migration | 1.2127 | 1.2907 | 1.6296 | 1.39 | 1.4496 | 1.3984 | 1.5827 | 1.8331 | 1.5598 | 1.5032 | 1.4754
All Fast (Ideal) | 1.3226 | 1.5429 | 1.9712 | 1.7016 | 2.2399 | 1.9382 | 2.2755 | 2.2808 | 1.9131 | 2.4203 | 1.9292
16GB fast memory
Worse than All Slow
as page migration throughput is low
40% Runtime Improvement

## Slide 16: Broad Applicability Results
Chart: Fast Memory Size
| 4 | 8 | 12 | 16 | 20 | 24 | 28
All Slow | 1 | 1 | 1 | 1 | 1 | 1 | 1
Stock Linux | 0.90846 | 0.95943 | 1.0249 | 1.092 | 1.1597 | 1.274 | 1.6382
Optimizaed Page Migration | 1.0917 | 1.1638 | 1.3234 | 1.4754 | 1.6186 | 1.7609 | 1.8786
All Fast(Ideal) | 1.9292 | 1.9292 | 1.9292 | 1.9292 | 1.9292 | 1.9292 | 1.9292
Fast memory size (4GB to 28GB) versus benchmark footprint (32GB)
45% Runtime Improvement
Performance Degradation

## Slide 17: Summary
Existing page migration mechanism is inefficient
  It utilizes only 4% hardware bandwidth
  It can lead to performance degradation in heterogeneous memory management
Our optimizations improve page migration throughput
  14.6x page migration throughput improvement
  Up to 45% end-to-end runtime speedup
High-performance page migration is essential to heterogeneous memory management

## Slide 18: Questions?